## Slide 1: The Game Of Life
The CDM-16 project made by Anna Shemchuk & Egor Dashkovsky, 24216.

## Slide 2: Standard rules
1. Living cells nearby are neighbours
2. 3 neighbours - a dead cell comes to life
3. 2, 3 neighbours – a living cell continues to live
4. Other cases lead to death

## Slide 3: Software

## Slide 4: 4 stages of software implementation
Naive implementation
Encoding a cell in 4 bits + Lookup Table (LUT)
Boolean function instead of LUT
Packing four cells into a uint16_t (two-byte words)

## Slide 5: 1. Naive realization
The field is represented as a two-dimensional array uint8_t field[16][16].
The state of each cell is stored as 0 (dead) or 1 (alive).
A nested loop over the X and Y axes is used to iterate over all 256 cells.
For each cell:
The number of live neighbours is counted by checking the eight surrounding elements of the array.
The following condition is checked:
The result is written using double buffering.
Condition:

## Slide 6: 2.1 Encoding a cell in 4 bits + Lookup Table (LUT)
Cell
0bvsss, where
v - stores whether the cell is alive or dead,
sss - is the number of neighbours
8 (0b1000) or 0 (0b0000) neighbours will be dead in the next generation.

## Slide 7: 2.2 Lookup Table (LUT)
| 0
| 0
| 0
| 1
| 0
| 0
| 0
| 0
| 0
| 0
| 1
| 1
| 0
| 0
| 0
| 0
0b_0000
0b_0001
0b_0010
0b_0011
0b_0100
0b_0101
0b_0110
0b_0111
0b_1000
0b_1001
0b_1010
0b_1011
0b_1100
0b_1101
0b_1110
0b_1111
abcd

## Slide 8: 3. Boolean Function Instead of LUT
PDNF function for LUT: (0b_abcd: 0b_0011 | 0b_1010 | 0b_1011)
f(a, b, c, d) = (¬a ∧ ¬b ∧ c ∧ d) ∨ (a ∧ ¬b ∧ c ∧ ¬d) ∨ (a ∧ ¬b ∧ c ∧ d)
Boolean Function Minimization:
f(a, b, c, d) = ¬b ∧ c ∧ (d ∨ a)
Code implementation: (conclusion.c)

## Slide 9: Packing Four Cells into uint16_t (Two-Byte Words)
Field:
Each 16-bit word packs four 4-bit cells of the form 0b_vsss_vsss_vsss_vsss
Encoding of four cells:
Function modification for 4 cells:
(conclusion.c)

## Slide 10: Source code files
1. main.c, while(1) cycle

## Slide 11
2. life.c, next_gen() function

## Slide 12
3. conclusion.c, next_state() function

## Slide 13
4. interrupts.c, KB_ISR()

## Slide 14
5. print.c, print() function

## Slide 15
6. start.asm

## Slide 16: Hardware

## Slide 17
1. CDM-16 with Von Neumann Architecture

## Slide 18
2. Playing Field

## Slide 19
3. Game Buttons Controls

## Slide 20
4. Cursor Controller

## Slide 21
5. Memory-mapped register selectors

## Slide 22
6. Interrupt Controller

## Slide 23: The result of our work (speed up 4x)